## Slide 1
ARCHITECTURE DIAGRAM
VitalTwin - System Architecture
1 · PHYSICAL PATIENT & DATA
⌚ Smartwatch
HR · SpO₂ · skin temp · steps (1 min)
🩸 CGM sensor
Glucose every 5 min
🩺 BP cuff
Systolic / diastolic, 3×/day
📋 EHR & labs
HbA1c · lipids · history · meds
📝 Patient log
Meals · exercise · sleep
2 · INGESTION & TWIN SYNC
Stream ingestion
Resample to 5-min windows
Interpolate gaps, de-noise
pandas pipeline (twin/data.py)
State estimation
EWMA blend of EHR + sensors
Resting HR · BP · fasting glucose
(twin/sync.py)
Physiological calibration
Fit insulin sensitivity SI and
basal glucose Gb to CGM
SciPy Nelder-Mead least squares
RMSE → sensor-noise level
3 · DIGITAL TWIN CORE
Twin state store
Patient profile + calibrated parameters
Physiology engine (mechanistic)
Bergman minimal model: glucose-insulin,
meals, exercise, metformin (1-min ODE)
Lifestyle model: weight · BP · HR · LDL
· HbA1c (ADAG) week-by-week
AI / ML engine (data-driven)
Calibrated HistGradientBoosting:
10-yr T2D & CVD risk (AUC 0.87 / 0.82)
Counterfactual risk-driver explainer
IsolationForest + personal z-score
+ clinical limits → alerts
4 · APPLICATIONS (STREAMLIT)
🧬 Twin state
Sync view & calibration fit
📡 Live monitoring
Vitals replay + alert feed
⚠️ Risk drivers
Explainable 10-yr risk
🔮 What-if simulator
Compare plans over 12-52 wks
🩸 Glucose twin
Plan a day: meals, walk, meds
Closed loop: clinician / patient chooses an intervention on the twin → applied to the real patient → new sensor data re-syncs and re-calibrates the twin